## Slide 1: A Convolution Accelerator for OR1200
Dawei Fan

## Slide 2: Contents
Introduction
1
Methodology
2
RTL Design and Optimization
3
Physical Layout Design
4
Conclusion
5

## Slide 3: Introduction
What is convolution?
  Convolution is defined as the integral of the product of the two functions after one is reversed and shifted. The convolution operation of f and g is denoted as f∗g.

## Slide 4: Introduction
Discrete Convolution
  Defined on set Z or Z+ , rather than R
  Convolution is the array of the sum of the product of two arrays after one is reversed and shifted.

## Slide 5: Introduction
What is convolution used for?
  It shows the information of relevance, which is similar to cross-correlation
  Applications in probability, statistics, signal processing
  Computer vision, image processing
  Convolution Code
    Error-correcting code

## Slide 6: Introduction
Motivation
  Convolution could be completed in software program, DSP
  A dedicated convolution accelerator could improve performance.

## Slide 7: Methodology
1. Read OR1200 specifications and related RTL code. Study convolution algorithm further.
2. RTL source code.
3. Function verification in DVE.
4. Repeat step 2-3 to optimize RTL source code.
5. Physical design with ICC and post layout verification.

## Slide 8: RTL Design and Optimization
Convolution.v
3.1
3.0
2.0
1.0

## Slide 9: RTL Design and Optimization
A basic implementation (1.0)
  Input: two arrays of 8 elements, 8-bit
  Output: an array of 15 elements, 16-bit

## Slide 10: RTL Design and Optimization
a[8]
b[8]
a_new[15]
b_new[15]
result[15]
invert
padding zeroes
input
output

## Slide 11: RTL Design and Optimization
Defects in 1.0
  When using arrays as input, there will be errors unless adding “-sverilog” option
  Too many ports
  Not scalable

## Slide 12: RTL Design and Optimization
Adding read and write (2.0)

## Slide 13: RTL Design and Optimization
Adding read and write (2.0)
  Sample input:
    a[] = {1,4,5,8,6,9,11,2}
    b[] = {31,25,9,7,16,19,3,2}
  Sample output:
    result[] = {3e, 187, 23c, 20c, 24c, 2ae, 2d2, 218, 183, 131, ca, 7b, 29, b, 2}16

## Slide 14: RTL Design and Optimization
Combine calculation and write (3.0)

## Slide 15: RTL Design and Optimization
Combine calculation and write (3.0)
    Write after calculation (2.0)
    Write during calculation (3.0)

## Slide 16: RTL Design and Optimization
Final RTL code (3.1)
  Minor changes: change “integer” type to a 4-bit register.
  Input: din, 16-bit
  Output: dout, 32-bit
  Control signals:
    Clk: clock
    Rst: reset data
    Rd: read input data
    Ena: begin calculation and write
    Busy: indicating calculation and write is in process

## Slide 17: RTL Design and Optimization
Final RTL code (3.1)

## Slide 18: RTL Design and Optimization
Final RTL code (3.1)

## Slide 19: Physical Layout Design
IC Compiler Design Flow
  Generate convolution_dc.v from DC
  Modify scripts:
    Change libraries path
    Change routing parameters
  Generate gds, FRAM, CEL

## Slide 20: Physical Layout Design

## Slide 21: Physical Layout Design
Area and Power report

## Slide 22: Conclusion
Design a convolution accelerator for OR1200 CPU
Verify basic functions in DVE waveform
Make optimizations in RTL to reduce area
Implement physical layout according to ICC design flow

## Slide 23
Thank You !